EFI Device Tree Fixup Protocol
Heinrich Schuchardt
CC-BY-SA-4.0

---
Motivation
Linux device-trees tend to be
neither forward nor backwards compatible.
E.g. commit bbc4d71d6354,
“net: phy: realtek: fix rtl8211e rx/tx delay config“
- Broke booting with old device-trees on boards with
  Allwinner 64bit SoCs.
- New device-trees are not compatible with existing U-Boot drivers.

---
Solution Idea
- GRUB has a 'devicetree' command but lacks fixups.
- Linux kernel distribution packages contain kernel image and device-trees.
- grub-mkconfig already updates grub.cfg concerning kernel binary and initial RAM disk.
- Let grub-mkconfig manage the device-tree too.
- /model node can be used to identify board specific dtb.
- Let 'devicetree' command call an EFI protocol for fixups.

---
EFI Device Tree Fixup Protocol
typedef EFI_STATUS (EFIAPI *EFI_DT_FIXUP) (
    IN EFI_DT_FIXUP_PROTOCOL *This,
    IN VOID *Fdt,
    IN OUT UINTN *BufferSize,
    IN UINT32 Flags
    );
Flags:
- EFI_DT_APPLY_FIXUPS	Add nodes and update properties
- EFI_DT_RESERVE_MEMORY	Reserve memory
- EFI_DT_INSTALL_TABLE	Install the device-tree as configuration table

---
Status
- A draft specification is available at https://github.com/U-Boot-EFI/EFI_DT_FIXUP_PROTOCOL
- The U-Boot v2021.04 tree contains the implemementation.
- Next steps
  - Patch GRUB
  - Include in EBBR